## Slide 1: Satellite-based Total Cloud Cover retrieval to support automatic cloud amount measurement
Hwan-Woo Lee, Geun-Hyeok Ryu
Satellite Analysis Division, NMSC, KMA
20th December 2017 (Wed.)

## Slide 2
How we measure cloud amount
○ Total cloud cover is the fraction of the sky covered by cloud of any type or height above the ground. Partial cloud amount is the fraction of the sky covered by each type or layer of cloud as if it was the only type or layer of cloud in the sky. If a number of different layers of cloud are present the partial amount of each one will be reported. The sum of partial cloud amounts may exceed the total cloud amount or indeed exceed 100% of the sky.
○ Total cloud cover is reported in decile :
- 0 tenth represents the complete absence of cloud
- 1 tenth represents a cloud amount of 1 tenth or less, but not zero
- 5 tenths represents a cloud amount of half
- 9 tenths represents a cloud amount of 9 tenths or more, but no full cloud cover
- 10 tenths represents full cloud cover with no breaks
○ Currently, Total cloud cover is only reported from stations where the human observer is present.

## Slide 3
Background
○ Automatic measurement trend
- From the age of synoptic observation which depend only on man-made observation,
To real-time observation using satellite, radar, aircraft with on-board advanced equipment
○ Automatic measurement in KMA
- NMSC has been operationally retrieving the TCC at tenth (0 to 10) from the COMS
- To support automated observation, NMSC improved the operational CA estimation algorithm based on COMS at 2015
- New technology such as Artificial Intelligence (AI) is required to retrieval meteorological parameters and next-generation satellite data are also available.
- NMSC developed total cloud cover retrieval based on random forest method using Himawari-8 data at 2017
Notes: due to development of measuring technology

## Slide 4
Total cloud cover by different viewing angle
Due to the difference in viewing angle depending on the location of the cloud
Satellite
Human

## Slide 5
Difference btw Satellite and human observation
Viewing angle
Cloud shape

## Slide 6
Total Cloud Cover Estimation Algorithm by COMS
- The retrieval process of COMS TCC (CA) algorithm is presented in Figure 1
- CF is satellite-observed cloud fraction and CA is ground-observed cloud cover.
- TCC (CA) is retrieved from the CF using the Kassianov et al.(2005) method which consider observation condition and the horizontal and vertical size of the cloud to compare with human-observed cloud amount
- Diagram of the COMS TCC estimation algorithm.
- CLD is cloud detection information and CTP is cloud top pressure.

## Slide 7
Cloud Amount from COMS
COMS TCC
Clear (0~2)
Partly Cloudy (3~5)
Mostly Cloudy (6~8)
Cloudy (9~10)
17th July 2016 15UTC
IR image

## Slide 8
Performance of operational CA from COMS
- COMS retrieved CA was compared with ground observation TCC (CA) by humans in Seoul, Korea from Dec. 2013 to Nov. 2014 to investigate the possibility of automated observation of CA from COMS observation.
- The ground observation of TCC is made every 3 hours from 12 to 18UTC and every hour for the rest of time, for ten minutes before the on-time observation hour.
- So, the collocation dataset was made by averaging 3X3 pixels of COMS TCC (CA) from the closest ground observation station within 15 minutes before the ground observation time
- CA derived from the COMS algorithm compares quite well with CA from visual observation with a correlation coefficient of 0.85, even though the COMS overestimates CA with Bias and RMSE of 0.51 and 2.33 respectively.
- However, the frequencies of CA from the COMS are mostly concentrated in 0 (clear) and 1 (cloudy), which may be caused by the spatial resolution of the COMS and the difference of observation method.
Comparison of the number density distribution between operational CA from the COMS and visual observation CA in Seoul from Dec. 2013 to Nov. 2014.
※ 0, ±1, ±2  difference btw. Grd-TCC and Satellite-TCC
Notes: - Compared to the visual observation, the COMS tends to overestimate CA especially in winter season, when the cold air from the north latitudes expands to the Korean Peninsula.
- Figure 5 shows an example of cloud detection at 2045UTC on 8th Jan., 2014. Compared to the IR image, the cloud mask image seems to misidentify clouds especially over the middle and north regions of Korea and Mongolia.
- Large bias was occurred in Seoul: CA from COMS was 8, whereas visual observation was 0.

## Slide 9
Total Cloud Cover from Himawari-8
◈ Random Forest
Random forests are an ensemble learning method for classification, regression and other tasks.
Random forests operate by constructing a multitude of decision trees at training time and outputting the class.
The class is the mode of the classification or mean prediction of the individual trees.
R language / H2O Library
◈ Training data set and Validation data set
 | Training data set | Validation data set
Grd. observation site | 22 human observation sites | 
Data sampling | 9x9 pixels (18x18 km2) Day only (00 UTC ~ 09 UTC) and exclude fog cases | 
Period | Jan. ~ Dec. 2016 (1 Year ) | Sep. ~ Dec. 2015 (4 months)
Data number | 68,061 cases | 22,688 cases
Option | nTree = 256, Depth = 30 | 
Variables | 51 variables (mean brightness temperature difference between IR channels) (Himawari-8 Ch.11~15) | 
Target output | Modified Total Cloud Cover at Ground | Total Cloud Cover

## Slide 10
Modified Total Cloud Cover at Ground site
◈ Ground Observed TCC
Every 1 or 3hourly reported at 22 human sites
Subjective Observation - Unbalanced  0 or 10 tenths are dominant - 1, 5, 9-tenths are relatively small
CA : TCC before correction
CA’ : TCC after correction
Comparison between before and after correction
 Complement 1, 5, 9-tenths TCC frequencies
◈ Ground-TCC Correction
Notes: 각 주/야간, 여명/황혼기 때 채널특성을 고려,
경계값 검사 조합을 통해 구름탐지 (CLD) 수행
화소 구름탐지 유무에 따라 13종 산출물에 영향이 끼침

## Slide 11
Himawari-8 TCC Retrieval Model
Sample image for Himawari-8 TCC
Preprocessing step - Remove snow cover area - Input data for RF model
Determining TCC step (1 ~ 3) - Decide TCC from successive RF model (1~6)

## Slide 12
Validation Random Forest Model
◈ Validation
Period: September ~ December 2015 (daytime only 09~18 KST)
Sites : 22 sites (Seoul , Jeju etc.)
Comparison nearest pixel with observation site
 | 0~10 | 1~9
±0 | 43.9% | 13.4%
±1 | 74.5% | 39.4%
±2 | 89.3% | 51.7%
Total | 100.0% | 60.4%
Bias | RMSE | Corr.
-0.05 | 1.58 | 91%
※ 0, ±1, ±2  difference btw. Grd-TCC and Satellite-TCC

## Slide 13
Total Cloud Cover from Himawari-8
Himawari-8 TCC
COMS TCC
Clear (0~2)
Partly Cloudy (3~5)
Mostly Cloudy (6~8)
Cloudy (9~10)
17th July 2016 15UTC
IR image

## Slide 14
Sample results : Snow cover
Himawari-8 TCC
14th Jan. 2017 07UTC
Himawari-8 Natural RGB

## Slide 15
Sample results : Day and night
Natural RGB
Grd. Obs.
Grd. Obs.
27th July 2017 03UTC (daytime)
22th June 2017 15UTC (nighttime)
Himawari-8
Himawari-8
Airmass RGB from Himawari-8

## Slide 16
Validation and Comparison (Jan. 2017)
COMS
Validation (0~ 10 tenths)
Validation (1~9 tenths)
 | Bias | RMSE | Corr. | PC ±0 | PC ±1 | PC ±2
COMS | -0.20 | 1.96 | 89% | 44.9% | 68.1% | 84.5%
Himawari-8 | -0.22 | 1.74 | 90% | 43.5% | 71.5% | 87.2%
Himawari-8
Similar to Grd. Obs.
 | PC ±0 | PC ±1 | PC ±2 | Total
COMS | 6.5% | 20.5% | 29.9% | 37.8%
Himawari-8 | 13.7% | 37.3% | 50.0% | 60.9%

## Slide 17
Time series
◈ Time series of TCC at specific site (1st ~ 7th March 2017)
Daejeon
Jeju
Day (00UTC ~ 09UTC)
Night (10UTC ~ 08UTC)

## Slide 18
Summary
- Total Cloud Cover (Cloud Amount) algorithm is developed using Random Forest model over the Korea region based on Himawari-8 observation
1. Training RF model (Jan. ~ Dec. 2016), validation RF model (Sep. ~ Dec. 2015)
2. Apply successive RF decision to overcome unbalanced data distribution
- Accuracy Improvement: ±2  87%, especially 1~9 tenths most improved when compared with COMS TCC
- Support automatic cloud amount measurement since September 2017
Notes: 인간수준의 결과

## Slide 19: Thank You