## Slide 1: Introduction to the Service Plans of Geo-KOMPSAT-2A Satellite
Sung-Rae Chung
csr@korea.kr
National Meteorological Satellite Center
Korea Meteorological Administration

## Slide 2: GK-2A/AMI and Level-2+ Products
1
2
Data Service Plan and Summary

## Slide 3
GK-2A/AMI and Level-2 Products

## Slide 4: GK-2A, the World’s Next Generation of Geo-Meteo Satellite
Advanced Meteorological Imager (AMI)
Higher spectral resolution with 16 channels can retrieve new products to detect meteorological phenomena
New and rapid updated information to exploit the phenomena can be given every 10 min. for Full Disk and every 2 min. for East Asia area with low latency below 1 min.
Operation flexibility for the local area selection and scheduling can track and see the hazardous phenomena
Launched: 5 December 2018
2017
2019
2018
2013
2014
2015
2016
System Integration
Module integration
Bus design and review
Launch/IOT/OPS
Kick-off
Launch
CDR
TRR
Test
AMI PSR
SRR
PDR
System
Req. analyss
Preliminary
Design
Critical
Design
payload
test
AIT
Prep. Launch
IOT, Ops

## Slide 5: GK-2A AMI
AMI (Resolution) |  | ABI | AHI
1 blue | 0.47 (1km) | 0.47 | 0.46
2 green | 0.511 (1km) |  | 0.51
3 red | 0.64 (0.5km) | 0.64 | 0.64
4 | 0.856 (1km) | 0.865 | 0.86
5 | 1.38 (2km) | 1.378 | 
6 | 1.61 (2km) | 1.61 | 1.6
 |  | 2.25 | 2.3
7 | 3.830 (2km) | 3.90 | 3.9
8 | 6.241 (2km) | 6.185 | 6.2
9 | 6.952 (2km) | 6.95 | 7.0
10 | 7.344 (2km) | 7.34 | 7.3
11 | 8.592 (2km) | 8.50 | 8.6
12 | 9.625 (2km) | 9.61 | 9.6
13 | 10.403 (2lkm) | 10.35 | 10.4
14 | 11.212 (2km) | 11.2 | 11.2
15 | 12.364 (2km) | 12.3 | 12.3
16 | 13.31 (2km) | 13.3 | 13.3
vs. AHI
- addition 1.38 m (NIR)
- subtraction 2.3 m (NIR)
1.38 m : favorable for cirrus cloud detection, cloud type and amount
2.3 m : favorable for Land/cloud Properties

## Slide 6: Observation Area and Schedule
  Full Disk (FD)
  Extended Local Area (ELA) : 3800 X 2400 km (EW X NS)
  Local Area (LA) 1000 X 1000 km
1 FD + 5 ELA + 5 LA : 10 min
The official request of target area observations by global users over the Asian Pacific region (RA II and RA V) will be available
  The first priority is the disasters monitoring over Korean Peninsular, such as typhoon, wild fire etc
  Global users submit official request form defining specific measurement area via designated web page (or email)
  Decision will be made before disseminating images via designated web page
Notes: KMA will operate 10 minute timeline with one full disk image, and five ELA (Extended Local Area) and five LA (local area).
With the LA scene, KMA can observe the moving targets such as typhoon, and specific event like volcano eruption.
For the target area observation, KMA will receive the official request for specific area observations by global users over the Asian Pacific region (RA II and RA V).
  Global users submit official request form defining specific measurement area via designated web page (or email)
  Decision will be made before disseminating images via designated web page

## Slide 7: GK-2A/AMI Level-2 Products
Primary Products
Vertical
Temperature
Profile
Vertical
Moisture
Profile
Instability Index
Cloud Detection
Fog
Sea Surface
Temperature
Land Surface
Temperature
Snow Cover
Sea Ice Cover
Aerosol
Detection
Asian
Dust
Detection
Asian
Dust
Optical
Depth
Aerosol
Optical
Depth
Volcanic Ash
Detection,
Height &
Mass
Radiance
Atmospheric
Motion
Vector
Total Ozone
Cloud Top Temperature
Cloud Top Pressure
Cloud Top Height
Rainfall Rate
Convective Initiation
Cloud Phase
Secondary Products
Fire Detection
Vegetation Index
Vegetation Green Fraction
Surface Emissivity
Surface Albedo
Cloud Effective Radius
Cloud Liquid Water Path
Cloud Ice Water Path
Cloud Layer/Height
Probability of Rainfall
Snow Depth
Ocean Current
Cloud Type
Cloud Amount
Cloud Optical Depth
Rainfall Potential
Aerosol Particle Size
Visibility
Absorbed SW Radiation (SFC)
Downward SW Radiation (SFC)
Reflected SW Radiation (TOA)
Downward LW Radiation (SFC)
Upward LW Radiation (SFC)
Upward LW Radiation (TOA)
Aircraft Icing
Overshooting Top Detection
SO2 Detection
Total Precipitable Water
Clear Sky Turbulence
Notes: This table shows 52 GK-2A/AMI geophysical products with many kinds of information such as scene/surface, cloud/rainfall, radiation/aerosol, and atmospheric condition and aviation.
These products has been validated to evaluate the maturity and improve their algorithms.

## Slide 8: Pre-launch Status of Algorithms
Pre-launch test Level-2 product algorithms
I
Implement Level-2 product processing system
II
Improve the algorithms and processing system through feedback process between users and developers
III
To begin with analyze the performance of the related products for monitoring hazardous weather events in cooperation with KMA users
Implement the integrated algorithms in the operational demonstration environment for long-term period
Investigate the accuracy if meet the users requirements and evaluate their maturities
Test the level-2 product algorithms in the test-bed system
Improve the algorithms through review processes with the developers and the international review team

## Slide 9: Reference Observational Data for Validation
Dropsonde
GVR (radiometer)
Cloud particles
Aerosol
GEO-LEO Satellites
Clouds
Winds
Rain rate
Aerosol/Dust
SST
T, q profiles
Ground GNSS
Network
Research Airplane
Research Vessel
TPW
KMA’s Observation Network
KMA Ground Reference Observatory
Automatic Weather Stations
Radiosonde stations
Buoy stations
Aerosol and Ozone monitoring
Lightning network
KMA GAW Stations
Aerosols
Greenhouse Gases
Precipitation Chemistry
Atmospheric Radiation
Stratospheric Ozone & UV

## Slide 10: Cloud Detection
    Retrieval Method: Conventional Multi-spectral Threshold Test
    Spatial resolution: 2 km
    Temporal resolution: 10 minutes
    Products
    3 Categories (Cloud / Probably Cloud / Clear)
    Intermediate products (19 tests)
    Applications
    Preprocessing step in various satellite applications : clear sky radiance, aerosol detection, land/sea surface temperature etc.

## Slide 11: Atmospheric Profile
    Retrieval Method: iterative physical retrieval using Optimal Estimation (OE) based on 1DVAR
    Spatial resolution: 33 FOVs (1FOV=2km)
    Temporal resolution: 2 minutes
    Products
    Temperature & Humidity profiles
    Total & Layer Precipitable Water
    Stability Indices (KI, SI, LI, TTI, CAPE)
    Total Column Ozone - clear sky, low clouds
    Applications
    Monitoring pre-environment condition of convective clouds and heavy rain
clear sky

## Slide 12: Convective Initiation
    Retrieval Method: Object based
    Convective Cloud Mask
    Clustering of cloud pixel (Region growing method)
    Object tracking & Interest field test
    Spatial resolution: 2 km
    Temporal resolution: 2 minutes
    Applications
    Detecting the cloud object which could rapidly develop to bring severe weather within 2 hours.
    Usage of short-term forecast
04:20 UTC
06:00 UTC Radar

## Slide 13: Atmospheric Motion Vectors
    Retrieval Method
    Optimal target selection
    Height assignment
      CCC (using cloud top pressure) &
      RTM based methods (EBBT, CO2 slicing, etc.)
    Quality Control: Quality Indicator &
    Expected Error
    Spatial resolution: 1616 pixels (IR)
    4848 pixels (VIS)
    Temporal resolution: 30 minutes
    Applications
    Usage of NWP model
    Tracking cloud system and moisture movements

## Slide 14: Cloud Analysis
    Products
    Cloud Top Temperature/ Pressure/
    Height
    Cloud Phase / Type / Amount
    Cloud optical thickness (Day/Night)
    Cloud effective radius / water path
    Spatial resolution: 2 km
    Temporal resolution: 10 minutes
    Applications
    nowcasting through real-time monitoring of macro & micro clouds properties
CP
CTT
COT
CT
Ci
Cs
Dc
Ac
As
Ns
Cu
Sc
St

## Slide 15: Application Techniques using AMI Products and Others
Typhoon/Ocean
Surface/Hydrology
Nowcasting
Climate/Environment
Ocean environment
Sea surface wind and 3-D horizontal winds
Intensity change of tropical cyclone
Objective analysis of tropical cyclone
Forest Fire
Blending, Downscaling & Validation
Soil moisture & flood
Drought
Multi-platform precipitation merging
Satellite image prediction
Objective cloud analysis
Convective cloud life cycle
Aerosol peak height / surface concentration
Air quality modeling support
Climate study
Greenhouse gas monitoring
smoke
Notes: In parallel with the products retrieval effort, KMA is developing “application techniques” for nowcasting, Typhoon and ocean analysis, hydrology and land surface analysis, and climate and environmental applications.
To support satellite data users, this application project will make “user friendly information” based on GK-2A observation and level 2 products together with all available data, such as LEO satellite products, ground observations and NWP model data.
These results will be implemented on the “Meteorological Data Analysis system” with the analysis guidance for various satellite data users.

## Slide 16: Application: Nowcasting and Typhoon
Nowcasting
Combined CI and RDT monitoring technology
Quantification of phase error
Typhoon
Rainfall and wind speed along Typhoon’s Track
For 113 typhoons, we calculate the averaged rainfall and wind speed at every latitude (1o resolution) along the track, which will be the database for the percentile analysis
Spatial distribution of outputs along Typhoon’s track.
Notes: These are some examples of Nowcasting and Typhoon analysis we are developing. We are trying to develop or optimize the NWC-SAF RDT (Rapidly developing Thunderstorm) algorithm, so called K-RDT. Especially, K-RDT combine convective cloud initiation(CI) product and RDT algorithm technology. In the RDT image, red circle represents cells defined from original RDT. Orange circle represents new cells detected from CI. RDT products can support heavy rainfall analysis, tracking and forecast. Using the observed image and simulated cloud image, we can analyze the phase error of NWP forecast. Also, we are trying to optimize Advanced Drorak Technique. Typhoon analysis technique estimates the percentile of tropical cyclone-induced rainfall and wind intensity compared to historical TCs. We will provide the guidance and analysis tools for estimating the intensity change of TC using thermodynamic and dynamic predictors, such as maximum potential intensity (MPI), intensification potential (POT), ocean heat content (OHC), and so on.

## Slide 17: Expectation of Rapid Scan Observations
(a) 2017-08-02 03:50 UTC
(b) 2017-08-02 03:54 UTC
(c) 2017-08-02 03:56 UTC
(d) 2017-08-02 04:00 UTC
(e) 2017-08-02 06:00 UTC
Convective Initiation using rapid scan data (b, c) has a possibility of earlier detection of convective clouds than that using regular scan data (a, d)
2-min Rapid Scan Imagery
Notes: This slide 2 shows CI using rapid scan data (b, c) has a possibility of earlier detection of convective clouds than that using regular scan data(a, d).

## Slide 18: RGB Imagery
True color RGB
Airmass RGB
Dust RGB
Fog RGB

## Slide 19: Enhanced Capabilities from GK-2A/AMI Level-2+ Products
Increases thunderstorm warning lead time
Improves typhoon track & intensity analysis and forecast
Improves Asian dust monitoring
Improves aviation flight route planning
Data for NWP model data assimilation
Data for long-term climate monitoring

## Slide 20
Data Service Plan and Summary

## Slide 21: Data Service Plan
The timeline of GK-2A level 1B data and imagery regular services will be started in July 2019.
Level 2 data will be released after optimizing the algorithms using operational level 1B data. The timeline of level 2 products provision will be from end of 2019 step by step.

## Slide 22: Data Service Plan
Via GK-2A broadcast (< 3 minutes data latency)
  Broadcast all 16 channels in full resolution (UHRIT)
  Maintain L/HRIT broadcast corresponding to COMS five channels
Via Landline
  Real-time cloud service similar to HimawariCloud will be also provided (< 5 min data latency)
  GK-2A data also will be available in DCPC-NMSC (http://dcpc.nmsc.kma.go.kr)
L1 Data Format
  netCDF4 (for each channels) with GSICS information
L2 Data Format
  netCDF4 (for each products)
L1 Data Header Structure
General Information
Output Information
Pixel File Information
Projection Information
Star Measurement Information
INR Characteristics Information
Image Geometry Quality Information using Star Measurements
Registered Image Information
Quality Area Image Information

## Slide 23: Summary
GK-2A satellite was launched on 5 December 2018 successfully.
KMA/NMSC is just about to carry out in-orbit test of GK-2A satellite for upcoming 7 months.
After that, we are going to do regular services GK-2A imageries and products in sequence. It will be started from July 2019.

## Slide 24: Thank you!